## Slide 1
Forward Kinematics of Serial Manipulators
• Computation of end-effector pose from joint angles (theta_1, ..., theta_n)
• Systematic spatial transformation using 4x4 homogeneous transformation matrices

## Slide 2
Denavit-Hartenberg (D-H) Parameter Conventions
• Link length (a_i): distance along x_i from z_{i-1} to z_i
• Link twist (alpha_i): angle from z_{i-1} to z_i about x_i
• Link offset (d_i): distance along z_{i-1} from x_{i-1} to x_i
• Joint angle (theta_i): angle from x_{i-1} to x_i about z_{i-1}
[Table Data]:
| Joint i | theta_i (deg) | d_i (mm) | a_i (mm) | alpha_i (deg) |
| 1 (Base) | theta_1 | 400 | 0 | 90 |
| 2 (Shoulder) | theta_2 | 0 | 500 | 0 |
| 3 (Elbow) | theta_3 | 0 | 400 | 0 |
| 4 (Wrist) | theta_4 | 150 | 0 | 90 |